## Slide 1: Lecture 5 SMART SENSORS and SMART ACTUATORS
CC5053NP - Cloud Computing and the Internet of Things

## Slide 2: Lecture Objectives
Sensors
Sensor Output
Smart Sensor
Smart Sensor Types
Smart Actuator and Types
Advantages of using Smart Sensors and Actuators
Case Studies

## Slide 3: What is a Sensor
Device that senses a physical quantity
This physical quantity becomes input to the sensor
Output of the sensor is an electrical quantity
Input is called measured quantity or “measurand”
Output (Electrical quantity)
Input (Physical quantity
or Measurand)
Sensor

## Slide 4: Sensor Output
The electrical output of a sensor can be one of the two types:
  Variation of an electrical parameter: Passive Sensor
  An electrical signal: Active Sensor
Variation of electrical parameter means
  Variation of resistance
  Variation of inductance
  Variation of capacitance
Electrical signal means
  Voltage signal, or
  Current signal

## Slide 5: Sensor Output
Notes: Reference: https://www.ti.com/document-viewer/lit/html/SSZTCA2

## Slide 6: Smart Sensors
Most of the sensors now labeled as Smart Sensors by the manufacturers:
“Smart Sensor is a micro-sensor integrated with appropriate micro-electronics, such that the final output is fully or easily compatible with the intended end device or devices”
Micro-
sensor
Micro-
electronics
Electrical output signal
Measurand
Integrated together
Indicating device
Display device
Storage device
Comm. device
Controller

## Slide 7: Level Of Integration
The output signal of smart sensor can have one of three forms:
  Analog
  Digital
  PWM
Extent/ level of integration of electronics with the micro-sensor:
  Lowest Level: Smart sensor with analog output
Low Level:
High Level:
Smart sensor with pwm output
Smart sensor with digital output
Higher Level: Smart intelligent sensor
Highest Level: Smart network sensor

## Slide 8: Smart Sensor with Analog Output
Micro- sensor
Analog signal processing Unit (ASPU)
Analog output signal
e.g. 0-1 V
0-5 V
4-20 mA
0-20 mA
Integrated together

## Slide 9: Smart Sensor with PWM Output
Micro-
sensor
ASPU
PWM
PWM output
Pulse width » Measurand
Integrated together
Analog voltage output

## Slide 10: Smart Sensor with Digital Output
Micro-
sensor
ASPU
ADC
Digital output
0 – 5V to
0-1023 values
Integrated together
Analog voltage output

## Slide 11: Smart Intelligent Sensor
Micro- sensor
ASPU
ADC
Processed data (serial or parallel)
Data processing unit (DPU)
Integrated together
DPU = Microcontroller
OR
uP + memory + I/O interface
Can be readily connected to a host computer or other digital system
Analog signal
Digital signal (data)

## Slide 12: Smart Network Sensor
Output: processed data on integrated network port in appropriate format
Micro-
sensor
ASPU
ADC
DPU
Comm.
interface
Network port
Data Network
output

## Slide 13: Smart Actuators
Communication/ PWM / Analog Interface
DPU / microController
Driver/ Power Stage
Actuator
“Smart Actuator is an actuator integrated with its own control and signal processing unit, so that it can enhance traditional actuators with intelligence, network communication, and control logic.”
Feedback
Set point

## Slide 14: Smart Actuators
Analog Actuators
  Accept analog input signals (e.g., 0–10V, 4–20mA).
  The actuator's position or speed varies proportionally to the input.
Digital Actuators
  Receive on/off or discrete position commands.
  Example: Open/close valve, forward/reverse motor.
PWM-Controlled Actuators
  Input is a digital pulse with varying duty cycle.
  Used in DC motor control, servo motors, lighting systems.

## Slide 15: Smart Actuators
Smart Intelligent Actuators
  Embedded microcontroller
  Can execute tasks autonomously (e.g., self-calibration, diagnostics).
  Often integrate sensors internally for feedback (position, temperature, etc.).
Smart Networked Actuators
  Allow multiple actuators to be controlled from a central Controller or cloud platform.
  Wireless Smart Actuators, Ideal for hard-to-reach locations or battery-powered systems.

## Slide 16: Advantages of Smart Sensor and Actuator (1)
User’s Convenience because of:
  No wiring
  Compact size
  No headache of selecting extra circuit
  No headache of designing extra circuit
Superior Performance because:
  External noise/disturbance effect is absent.
  Built-in device-specific circuits perform better
  Built-in feedback reduces error
  Built-in compensating circuits reduce sensitivity to temperature.

## Slide 17: Advantages of Smart Sensor and Actuator (2)
High Reliability because of:
  Reduced component count
  Reduced wiring
Cost Reduction because of:
  Concurrent production of electronics and sensor
  Mass production techniques

## Slide 18: Case Study #1
Smart Three-Terminal Temperature Sensor
Manufacturer: National Semiconductor Corporation Website: www.national.com

## Slide 19: LM35.…….
Major Specifications
LM35: Centigrade (or Celcius) Temperature Sensor
  Basic Range: 2 to 150 °C
  Output: 10 mV/°C
  Accuracy: ±0.2 °C (typical)
  Gives Linear Output
  Datasheet for different modes

## Slide 20: LM35.…….
Interfacing with Arduino

## Slide 21: Case Study #2
LCD with I2C Interface:
  Inter-Integrated Circuit: a two wire synchronous communication protocol
    Wires:
      SDA (Serial Data) – transfers data
      SCL (Serial Clock) – synchronizes data transfer
    Reduces number of pins needed to just 2 (SDA, SCL)
    Easier wiring and cleaner circuit design
    Can connect multiple I2C devices with just 2 wires and GND
  LCD: Liquid Crystal Display
    16x2 or 20x4 characters LCD
    Common I2C address: 0x27 or 0x3F

## Slide 22
Interfacing with Arduino
https://lastminuteengineers.com/i2c-lcd-arduino-tutorial/
Library:
  LiquidCrystal_I2C
  0X3F: Address
  16: Number of characters per line
  2: Number of Lines

## Slide 23: Case Study #3 Servo Motor
  a rotary actuator that precisely controls angular position.
  combines a DC motor, gearbox, position sensor (typically a potentiometer), and an internal control circuit.
  Smart Actuator
    Built-in feedback mechanism to self-adjusts to reach the commanded angle
    Receives PWM control signal
    Rotation Range
      1. Typically 0° to 180°
      2. Continuous mode 360°
  Robotics (arm joints, wheels)
  Drones, RC vehicles, Camera

## Slide 24
Interfacing with Arduino
Library: Servo.h
  Create Servo servo obj
  Attach control pin servo.attach(9)
  servo.write(angle)
https://lastminuteengineers.com/servo-motor-arduino-tutorial/
SG90 servo motor to the Arduino:
Red wire to the 5V pin
Black or Brown wire to the GND
Orange or Yellow wire to PWM pin

## Slide 25: End of the Lecture